## Slide 1: Samandar Khan Afridi Email: samandarkhanafridi@gmail.com Basic Arduino Programming
Contents:
Basic (void setup(),void loop())
Conditions/Loops (if,if-else,for,while,do-while)
Inputs/Outputs (pinMode,digitalRead,digitalWrite,analogRead,analogWrite)

## Slide 2: Basic:
The basic structure of Arduino programming is simple and is composed of two parts
setup()
loop()
Setup() function which initializes and sets the initial values, the loop() function does precisely what its name suggests, and the loops consecutively allowing your program to change and respond Use it to actively control the Arduino board

## Slide 3: Conditions/Loops:
if
Description: The if statement checks for a condition and execute the preceding statement or set of statements if the condition is ‘true’
Syntax:
if(condition){
//statement
}

## Slide 4
if-else
Description: The if…else allows greater control over the flow of a code then the basic if a statement by allowing multiple tests to be grouped an else clause (if at all exists) will be executed if the condition in the if statement results in falls. The else can proceed another if test, so that multiple, mutually exclusive tests can be run at the same time.
Symtax:
if (condition){
//do thing A
}
else if (condition2){
//do thing B
}
else {
// do thing C
}

## Slide 5
for
Description: The four statement is used to repeat a block of statements enclosed in curly braces an increment counter is usually used to increment and terminate the loop. The for statement is useful for any repetitive operation, and is often used in combination with arrays to operate on collections of data/pins.
Syntax: for(initialization; condition; increment){
// statement
}

## Slide 6
while
Description: A while loop will loop continuously and infinitely until the next until the expression inside the parenthesis() becomes false. Something must change the tested variable or the value are the while loop will never exit. This could be in your code such as an incremented variable or an external condition such as testing a sensor.
Syntax:
while (condition){
//statement
}

## Slide 7
do-while
Description: The do…while Loop works in same manner as the while loop, with the exception that the condition is tested at the end of the loop, So the loop will always run at least once.
Syntax:
do{
//statement block
}while(condition);

## Slide 8: Input/Output:
pinMode
Description: configures the specified pin to behave either as an input or an output.
Syntax:
void setup() {
pinMode(pin,mode);
//mode
//1. INPUT
//2. OUTPUT
}

## Slide 9
digitalRead
Description: Reads the value from a specified digital pin, either HIGH or LOW.
Syntax:
void loop() {
var=digitalRead(pinNumber);
//Returns
//HIGH(1) or LOW(0)
}

## Slide 10
digitalWrite
Description: Write a HIGH or LOW value to a digital pin.
Syntax:
void loop() {
digitalWrite(pin,value);
//returns nothing
}

## Slide 11
analogRead
Description: Read the value from the specified analog pin.
Syntax:
void loop() {
analogRead(pin);
//returns
}

## Slide 12
analogWrite
Description: Writes an analog value (PWM wave) to a pin.
Syntax:
void loop() {
analogWrite(pin,value);
//returns
}

## Slide 13
Thank You !